## Slide 1
Visualec • AI + Computer Vision + IoT Energy Management
VISUALEC
AI-Powered Vision-Based Adaptive Grid Energy Management System
Symposium Paper Presentation
MulticoreWare Annual R&D Symposium
Presenter: Sarvesh Sivasankaran Faculty Mentor: Anitha M
Rajalakshmi Engineering College
AI
Computer Vision
IoT
Energy Optimisation
SDG: 7, 9, 11

## Slide 2
Visualec • AI + Computer Vision + IoT Energy Management
Problem Statement & Motivation
Why adaptive zone-level appliance control is needed
OBSERVED GAP
Electrical appliances often remain ON in unused areas because control is manual, schedule-based, or too coarse-grained.
• Classrooms, labs and offices have dynamic occupancy patterns.
• PIR sensors only provide basic presence detection and limited spatial understanding.
• Manual switching fails when users forget or move between sections.
• Energy control must react at zone level, not only room level.
Need
An affordable system that detects actual occupancy and controls appliances only where needed.

## Slide 3
Visualec • AI + Computer Vision + IoT Energy Management
Research Objective & Contributions
Core outcomes expected from the Visualec prototype
Objective 1
Detect people from a live camera feed and map their position to room zones.
Objective 2
Control only zone-linked lights, fans or prototype loads using ESP32 and relays.
Objective 3
Monitor occupancy, relay state and estimated energy usage in real time.
Key Contributions
• Vision-based zone-level occupancy detection.
• AI-driven adaptive appliance switching logic.
• ESP32 Wi-Fi relay control layer.
• Dashboard for manual override and analytics.
• Scalable route from laptop-based MVP to edge-AI nodes.

## Slide 4
Visualec • AI + Computer Vision + IoT Energy Management
Proposed Visualec System
Laptop-based AI inference with ESP32 embedded actuation
1
Laptop camera captures the room.
2
YOLO detects people in the frame.
3
Zones identify where people are located.
4
Decision engine selects appliances.
5
ESP32 receives relay commands.
6
Dashboard monitors live status.
MVP Focus
Run computer vision on the laptop; use ESP32 as a reliable relay controller.

## Slide 5
Visualec • AI + Computer Vision + IoT Energy Management
System Architecture Diagram
Vision layer → AI decision layer → communication layer → embedded control

## Slide 6
Visualec • AI + Computer Vision + IoT Energy Management
Computer Vision & Zone Detection Methodology
How the system converts people detection into energy-control decisions
DETECTION METHOD
1
Capture frame using OpenCV.
2
Detect person class using lightweight YOLO.
3
Calculate bounding-box bottom-centre point.
4
Assign each person to the correct virtual zone.
5
Apply confidence threshold and filtering.
6
Use ON/OFF delays to prevent relay flickering.
Why bottom-centre?
It represents the person’s floor position better than the box centre, improving zone assignment.

## Slide 7
Visualec • AI + Computer Vision + IoT Energy Management
Hardware & Software Implementation
Practical MVP setup for demonstration
HARDWARE LAYER
Prototype Components
• ESP32 development board
• 4-channel relay module
• Laptop webcam as vision input
• Low-voltage bulbs or prototype loads
• Regulated 5V power supply
SOFTWARE LAYER
Software Stack
• Python + OpenCV + YOLO for AI detection
• FastAPI backend for control logic
• React/Next.js dashboard for monitoring
• SQLite for logs and analytics
• HTTP/WebSocket for communication
Relay Mapping
Zone 1 → Relay 1
Zone 2 → Relay 2
Zone 3 → Relay 3
ESP32 Role
Receives Wi-Fi commands, validates relay IDs, switches GPIO outputs and returns acknowledgement.

## Slide 8
Visualec • AI + Computer Vision + IoT Energy Management
System Workflow Diagram
Continuous real-time loop for adaptive appliance control

## Slide 9
Visualec • AI + Computer Vision + IoT Energy Management
Prototype Operation & Dashboard
Real-time monitoring, override and analytics for the MVP
DASHBOARD MODULES
1
Live camera feed with zones
2
Detected people and occupancy count
3
Relay ON/OFF states
4
ESP32 connectivity
5
Automatic / manual mode
6
Energy estimate and logs
Control Modes
Automatic, manual, hybrid and emergency modes.

## Slide 10
Visualec • AI + Computer Vision + IoT Energy Management
Results & Energy-Saving Evaluation
Metrics to validate performance and energy impact
EVALUATION METRICS
1
Person-detection accuracy
2
Zone-assignment accuracy
3
Detection FPS
4
Relay response time
5
Occupancy-state stability
6
Estimated energy saved
Energy Formula
Energy consumed = Appliance power × Active runtime ÷ 1000
Traditional vs Adaptive Operation
4.5 kWh
Baseline
All ON
2.1 kWh
Visualec
Adaptive
2.4 kWh
Saved
Energy

## Slide 11
Visualec • AI + Computer Vision + IoT Energy Management
Limitations, Edge Deployment & Future Scope
Current boundaries and the path to scalable research deployment
Current Limitations
• Accuracy depends on camera angle and lighting.
• Occlusion affects distant-person detection.
• Laptop is required for full YOLO MVP.
• Energy values are estimates without smart metering.
• Certified safety is required for mains deployment.
Future Enhancements
• Multi-camera and multi-room support.
• Smart meter and current-sensor integration.
• Cloud analytics and long-term reports.
• Predictive energy optimisation.
• Campus-scale building-management integration.
Edge-AI Research Extension
A compressed ESP32-S3 edge node can use a quantized person-only micro-detector such as ESPDet-Pico. This is feasible for low-FPS occupancy detection, but the laptop-based system remains the stronger MVP for accurate multi-person detection and dashboard demonstration.

## Slide 12
Visualec • AI + Computer Vision + IoT Energy Management
Conclusion
Visualec combines AI, computer vision and IoT to control electrical appliances according to real zone occupancy.
• Reduces dependency on manual switching.
• Provides modular laptop-to-ESP32 architecture.
• Supports dashboard monitoring and analytics.
• Can scale toward distributed edge-AI nodes.
Smarter occupancy detection.
Adaptive appliance control.
Efficient energy utilisation.
Thank You
Questions & Discussion